## Slide 1: diODE or
By Cook, Darris Tajeim

## Slide 2: References
(n.d.). OR and AND logic gates made with diodes. Electronics Area. https://electronicsarea.com/or-and-and-logic-gates-with-diodes/
Cook, D. (n.d.). Wikipedia. Diode Logic. https://en.wikipedia.org/wiki/Diode_logic

## Slide 3: Function of the Circuit:
The diode OR circuit performs a logical OR operation on its inputs. If any of the inputs have a voltage greater than the diode's forward voltage drop (typically around 0.7V for standard silicon diodes), current can flow through that diode and reach the common output. If none of the inputs have a voltage above the diode's forward voltage, no current flows to the output.

## Slide 4: Usage of the Circuit:
Diode OR circuits find applications in various electronic systems where a logical OR operation is needed. Common applications include signal processing, control systems, logic circuits, and power distribution systems. Others would be Emergency Lighting Systems: Emergency lighting systems often have both battery and mains power sources. Diode OR circuits can be used to combine these sources, ensuring that the emergency lights are powered by either the mains or the battery, providing illumination in case of a power outage.

## Slide 5: Advantages:
Simplicity: Diode OR circuits are simple and easy to design with only a few components.
Cost-Effectiveness: Diodes are inexpensive, making the circuit cost-effective for basic logic operations.
Efficiency: Diodes have low power dissipation, making the circuit efficient for certain applications.
Fast Response: Diodes offer fast response times, contributing to the speed of logical operations.
Isolation of Inputs: Diode OR circuits provide a degree of isolation between input sources. Each input is effectively separated from the others, preventing a fault in one input from affecting the others.

## Slide 6: Disadvantages:
Voltage Drop: Each diode introduces a voltage drop (around 0.7V for silicon diodes), which can be significant and affect the input-output relationship.
Limited Precision: The voltage threshold for logical operation is determined by the diode's forward voltage, which is not a precise threshold compared to active electronic components.
Non-ideal Behavior: Real-world diodes may exhibit variations in forward voltage and other parameters, leading to deviations from the expected behavior.
Design Sensitivity: The performance of the diode OR circuit is sensitive to component values and characteristics. Small variations in diode parameters can significantly impact the behavior of the circuit, making it necessary to carefully design and select components.
Efficiency Losses: The voltage drop across diodes results in power dissipation, leading to energy losses and reduced overall efficiency, especially in high-power applications.

## Slide 7: Variations:
Reverse Diode OR Circuit: Uses diodes in the reverse direction, allowing current to flow when none of the inputs have a voltage, and blocking current when any input has a voltage.
Active OR Circuit: Integrates diodes with active components like transistors for improved precision and performance, mitigating the voltage drop issue.
Diode-Resistor OR Circuit: Combines diodes with resistors to modify the threshold voltage and enhance the circuit's accuracy.
Time-Delayed Diode OR Circuit: Incorporates capacitors and resistors in parallel with the diodes to introduce time delays in the logical OR operation. This is useful in applications where timing plays a critical role.
Diode-Resistor OR Circuit: Introduces resistors in series with diodes to modify the voltage thresholds for each input. This variation provides greater control over the OR logic operation.